2012 APRILIA RSV4 FACTORY APRC: Technical Specifications

| Engine type | Aprilia longitudinal 65° V-4 cylinder, 4-stroke, liquid cooling system, double overhead camshafts (DOHC), four valves per cylinder |
| --- | --- |
| Fuel | Unleaded petrol |
| Bore and stroke | 78 x 52.3 mm |
| Total engine capacity | 999.6 cc |
| Compression ratio | 13:1 |
| Maximum power at crankshaft | 180 HP (132.4 kW) at 12,250 rpm |
| Maximum torque at crankshaft | 115 Nm at 10,000 rpm |
| Fuel system | Airbox with front dynamic air intakes. Variable length intake ducts controlled via ECU. 4 Weber-Marelli 48-mm throttle bodies with 8 injectors and latest generation Ride-by-Wire engine management. Choice of three different engine maps selectable by the rider with bike in motion: T (Track), S (Sport), R (Road) |
| Ignition | Magneti Marelli digital electronic ignition system integrated in engine control system, with one spark plug per cylinder and “stick-coil”-type coils |
| Starter | Electric |
| Exhaust system | 4 into 2 into 1 layout, single oxygen sensor, lateral single silencer with engine control unit-controlled butterfly valve and integrated trivalent catalytic converter (Euro 3) |
| Alternator | Flywheel mounted 420W alternator with rare earth magnets |
| Lubrication | Wet sump lubrication system with oil radiator and two oil pumps (lubrication and cooling) |
| Transmission | 6-speed cassette type gearbox 1st: 38/16 (2.375) 2nd: 35/18 (1.944) 3rd: 28/17 (1.647) 4th: 32/22 (1,455) 5th: 34/26 (1,308) 6th: 33/27 (1,222) Gear lever with Aprilia Quick Shift electronic system (AQS) |
| Clutch | Multiplate wet clutch with mechanical slipper system |
| Primary drive | Straight cut gears and integrated flexible coupling, drive ratio: 73/44 (1,659) |
| Secondary drive | Chain: Drive ratio: 42/16 (2.625) |
| Traction management | APRC System (Aprilia Performance Ride Control), which includes Traction Control (ATC), Wheelie Control (AWC), Launch Control (ALC), all of which can be configured and deactivated independently. |
| Chassis | Twin-spar adjustable aluminium frame, with castings and pressings. Envisaged adjustments: headstock position and rake engine height swingarm pin height Öhlins adjustable steering damper |
| Front suspension | Öhlins Racing upside-down fork,  43-mm stanchions (with Tin surface treatment). Low profile forged aluminium radial caliper mountings. Completely adjustable spring preload and hydraulic compression and rebound damping. Wheel travel: 120 mm |
| Rear suspension | Double braced aluminium swingarm; mixed low thickness and sheet casting technology. Öhlins Racing mono-shock absorber with completely adjustable piggy-back in: spring preload, wheelbase, hydraulic compression and rebound damping. APS progressive linkage. Wheel travel 130mm |
| Brakes | Front: Dual 320-mm diameter floating stainless steel disc with lightweight stainless steel rotor and aluminium flange with 6 pins. Brembo monobloc radial callipers with 4 34-mm opposite. Sintered pads. Radial pump and metal braided brake hose |
|  | Rear: 220-mm diameter disc; Brembo floating calliper with two 32mm isolated pistons. Pump with integrated tank and metal braided hose |
| Wheel rims | Aprilia forged aluminium alloy rims, completely machined, 5 split spokes. Front:3.5”X17” Rear: 6”X17” |
| Tyres | Radial tubeless. Front: 120/70 ZR 17 Rear: 200/55 ZR 17 (alternative: 190/50 ZR 17; 190/55 ZR 17) |
| Dimensions (default settings) | Max. length: 2040 mm Max. width: 735 mm (at the handlebar) Max. height: 1120 mm Min. height from the ground: 130 mm Saddle height: 845 mm Centre to centre distance: 1420 mm Trail: 105 mm Steering angle:24.5° |
| Kerb weight | 179 kg * |
| Tank | 17 litres (4-litre reserve included) |

*Dry weight, without battery and fluids.

2012 APRILIA RSV4 R APRC: Technical Specifications

| Engine type | Aprilia longitudinal 65° V-4 cylinder, 4-stroke, liquid cooling system, double overhead camshafts (DOHC), four valves per cylinder |
| --- | --- |
| Fuel | Unleaded petrol |
| Bore and stroke | 78 x 52.3 mm |
| Total engine capacity | 999.6 cc |
| Compression ratio | 13:1 |
| Maximum power at crankshaft | 180 HP (132.4 kW) at 12,250 rpm |
| Maximum torque at crankshaft | 115 Nm at 10,000 rpm |
| Fuel system | Airbox with front dynamic air intakes. Variable length intake ducts controlled via ECU. 4 Weber-Marelli 48-mm throttle bodies with 8 injectors and latest generation Ride-by-Wire engine management. Choice of three different engine maps selectable by the rider with bike in motion: T (Track), S (Sport), R (Road) |
| Ignition | Magneti Marelli digital electronic ignition system integrated in engine control system, with one spark plug per cylinder and “stick-coil”-type coils |
| Starter | Electric |
| Exhaust system | 4 into 2 into 1 layout, single oxygen sensor, lateral single silencer with engine control unit-controlled butterfly valve and integrated trivalent catalytic converter (Euro 3) |
| Alternator | Flywheel mounted 420W alternator with rare earth magnets |
| Lubrication | Wet sump lubrication system with oil radiator and two oil pumps (lubrication and cooling) |
| Transmission | 6-speed cassette type gearbox 1st: 38/16 (2.375) 2nd: 35/18 (1.944) 3rd: 28/17 (1.647) 4th: 32/22 (1,455) 5th: 34/26 (1,308) 6th: 33/27 (1,222) Gear lever with Aprilia Quick Shift electronic system (AQS) |
| Clutch | Multiplate wet clutch with mechanical slipper system |
| Primary drive | Straight cut gears and integrated flexible coupling, drive ratio: 73/44 (1,659) |
| Secondary drive | Chain: Drive ratio: 42/16 (2.625) |
| Chassis | Twin-spar aluminium frame, with castings and pressings. Sachs steering damper |
| Front suspension | Showa upside-down fork, ( 43 mm stanchions. Aluminium radial caliper mountings. Completely adjustable spring preload, hydraulic compression and rebound damping. Wheel travel 120 mm |
| Rear suspension | Double braced aluminium swingarm; mixed low thickness and sheet casting technology. Sachs mono-shock absorber with completely adjustable piggy-back in: spring preload, wheelbase, hydraulic compression and rebound damping. APS progressive linkage. Wheel travel 130mm |
| Brakes | Front: Dual 320-mm diameter floating stainless steel disc with lightweight stainless steel rotor and aluminium flange with 6 pins. Brembo monobloc radial callipers with 4 34-mm opposite. Sintered pads. Radial pump and metal braided brake hose |
|  | Rear: 220-mm diameter disc; Brembo floating calliper with two 32mm isolated pistons. Pump with integrated tank and metal braided hose |
| Wheel rims | Front: Aluminium alloy rims, 6 split spokes 3.5”X17” Rear: Aluminium alloy rims, 5 split spokes 6”X17” |
| Tyres | Radial tubeless. Front: 120/70 ZR 17 Rear: 190/55 ZR 17 (alternative 190/50 ZR 17) |
| Dimensions | Max. length: 2040 mm Max. width: 735 mm (at the handlebar) Max. height: 1120 mm Min. height from the ground: 130 mm Saddle height: 845 mm Centre to centre distance: 1420 mm Trail: 105 mm Steering angle:24.5° |
| Kerb weight | 179 kg * |
| Tank | 17 litres (4-litre reserve) |

*Dry weight, without battery and fluids.