2012 APRILIA SHIVER 750 TECHNICAL SPECIFICATIONS

| Engine type | Aprilia V90 Longitudinal two cylinder 90° V, 4 stroke, liquid cooled, double overhead shaft timing controlled by a mixed gear/chain system, four valves per cylinder. |
| --- | --- |
| Fuel | Unleaded Petrol |
| Bore and stroke | 92 x 56.4 mm |
| Total engine capacity | 749.9 cc |
| Compression ratio | 11: 1 |
| Max power at the shaft | 95 HP at 9,000 rpm |
| Max torque at the shaft | 8.25 kgm at 7,000 rpm |
| Fuel system | Ride by Wire integrated engine control system. |
| Ignition | Digital electronic ignition integrated with injection system. |
| Starter | Electric |
| Exhaust | 2 in 1 system made entirely of stainless steel with three way catalytic converter and lambda probe |
| Alternator | 450 W at 6,000 rpm |
| Lubrication | Wet sump |
| Gearbox | 6 speeds, drive ratio: 1st 36/14 (2.57) 2nd 32/17 (1.88) 3rd 30/20 (1.5) 4th 28/22 (1.27) 5th 26/23 (1.13) 6th 25/24 (1.04) |
| Clutch | Multiple discs in oil bath with hydraulic control |
| Primary drive | Straight cut gears, drive ratio: 60/31 (1.75) |
| Secondary drive | Chain. Gear ratio: 16/44 |

| Chassis | Modular steel trellis connected with high resistance bolts to aluminum side plates. Modular rear frame. |
| --- | --- |
| Front suspension | Upside down fork with  43 stanchions. 120 mm wheel travel. |
| Rear suspension | Aluminum alloy swingarm with stiffener brace. Hydraulic shock absorber with adjustable rebound and preload. 130 mm wheel travel. |
| Brakes | Front: Dual  320 mm diam. wave stainless steel floating disc. Radial calipers with four pistons. Metal braided brake pipe. 2-channel Continental ABS system |
|  | Rear: 240 mm stainless steel wave disc. Single piston caliper. Metal braided brake pipe. |
| Wheel rims | Aluminum alloy Front: 3.50 X 17" Rear: 5.5 x 17" |
| Tyres | Tubeless radial; front: 120/70 ZR 17 rear: 180/55 ZR 17 |
| Dimensions | Max. length 2,265 mm Max. width 810 mm (at handlebar) Max. height 1,135 mm (at instrument panel) Saddle height 800 mm Centre to centre distance 1,440 mm Trail 109 mm Steering angle 25.7° |
| Tank | 15 litres |