2012 APRILIA TUONO V4 R APRC: Technical specifications

| Engine type | Aprilia longitudinal 65° V-4 cylinder, 4-stroke, liquid cooling system, double overhead camshafts (DOHC), four valves per cylinder |
| --- | --- |
| Fuel | Unleaded petrol |
| Bore and stroke | 78 x 52.3 mm |
| Total engine capacity | 999.6 cc |
| Compression ratio | 13:1 |
| Maximum power at crankshaft | 167.3 HP at 11,500 rpm |
| Maximum torque at crankshaft | 82 ft. lbs at 9,500 rpm |
| Fuel system: | Airbox with front dynamic air intakes. 4 Weber-Marelli 48-mm throttle bodies with 4 injectors and latest generation Ride-by-Wire engine management. Choice of three different engine maps selectable by the rider with bike in motion: T (Track), S (Sport), R (Road) |
| Ignition | Magneti Marelli digital electronic ignition system integrated in engine control system, with one spark plug per cylinder and “stick-coil” type coils |
| Starter | Electric |
| Exhaust system | 4 into 2 into 1 layout, single oxygen sensor, lateral single silencer with ECU-controlled bypass valve and integrated trivalent catalytic converter (Euro 3) |
| Alternator | Flywheel mounted 420W alternator with rare earth magnets |
| Lubrication | Wet sump lubrication system with oil radiator and two oil pumps (lubrication and cooling) |
| Transmission | 6-speed cassette type gearbox 1st: 39/15 (2,600) 2nd: 33/16 (2.063) 3rd: 34/20 (1,700) 4th: 32/22 (1,455) 5th: 34/26 (1,308) 6th: 33/27 (1,222) Gear lever with Aprilia Quick Shift electronic system (AQS) |
| Clutch | Multiplate wet clutch with mechanical slipper system |
| Primary drive | Straight cut gears and integrated flexible coupling, drive ratio: 73/44 (1,659) |
| Secondary drive | Chain: Drive ratio: 42/16 (2,625) |
| Traction control | APRC System (Aprilia Performance Ride Control), which includes Traction Control (ATC), Wheelie Control (AWC), Launch Control (ALC), all of which can be configured and deactivated independently. |
| Chassis | Aluminum dual beam chassis with cast and pressed sheet elements. |
| Front suspension | Sachs upside down front fork with  43 mm stanchions. Forged aluminum caliper mountings for radial calipers. Completely adjustable spring preload and hydraulic compression and rebound damping. Sachs steering damper. Wheel travel: 120 mm |
| Rear suspension | Double braced aluminum swingarm; mixed low thickness and sheet casting technology. Sachs piggy back monoshock with completely adjustable: spring preload and hydraulic compression and rebound damping. APS progressive linkage. Wheel travel: 130 mm |
| Brakes | Front: Dual 320 mm floating stainless steel discs with lightweight stainless steel rotor with 6 studs. Brembo radial calipers with 4  horizontally opposed 32 mm pistons. Sintered pads. Axial pump master cylinder and metal braided brake hoses. |
|  | Rear: 220-mm diameter disc; Brembo floating calliper with two 32 mm isolated pistons. Pump with integrated tank and metal braided hose |
| Wheel rims | Cast aluminum wheels with 3 split spoke design. Front.:3.5”X17” Rear: 6.00”X17” |

| Tires | Radial tubeless. Front: 120/70 ZR 17 Rear: 190/55 ZR 17 (alternative: 190/50 ZR 17; 200/55 ZR 17) |
| --- | --- |
| Dimensions (default settings) | Max. length: 81.2 inches / 2065 mm Max. width: 31.5 inches / 800 mm (at the handlebar) Max. height: 42.9 inches / 1090 mm Min. height from the ground: 4.92 inches Saddle height: 32.8 inches / 835 mm Wheelbase: 56.8 inches / 1445 mm Trail: 4.23 inches / 107.5 mm Steering angle:25° |
| Dry weight | 403 pounds / 183 kg |
| Fuel Tank | 4.5 Gallons (1 gallon reserve included) / 17 liters (4 liter reserve) |