Product Information: BeoPlay A9

Design, dimensions and materials

Designer: Øivind Alexander Slaatto

Materials: Aluminium, fabric, wood, plastic

Dimensions:

- On wooden legs: 	Diameter x Height x Footprint depth: 70 x 91 x 41 cm

- On wall: 		Diameter x Depth (incl. wall bracket) 70 x 21.3 cm

Weight: Approx. 14.5 kg (incl. legs) 13.7 kg (without legs)

Colours: Cabinet is available in white; removable speaker fabric cover is white as standard, and also available in silver, green, red, black and brown; solid wooden legs are beech as standard, and also available in oak or teak

Accessories: Wall bracket, additional fabric covers, additional solid wood legs

Design features:

- Minimalistic design that builds on the basic shape of the circle

- Bass reflex port on back incorporates handle for easy carrying and wall mounting

- Front sound grill, behind the fabric cover, is perforated to create a uniform plane that does not reveal speaker locations. The Fibonacci pattern also makes an appealing cover in itself – without the fabric

- Stands on floor or hangs on wall

Sound components and specs

Principle: Bass reflex system

Speakers:

- 1 x 8” woofer

- 2 x 3” midrange

- 2 x ¾” tweeters

Amplifier: 480 watts digital Class D amplifier system with separate amps for all speakers

- 1 x 160 watts class D for bass

- 2 x 80 watts class D for midrange

- 2 x 80 watts class D for treble

Adaptive Bass Linearisation: Bang & Olufsen’s patented technology for speaker systems delivers accurate and powerful bass at all listening levels. The digital algorithm constantly monitors bass levels, and automatically adjusts the bass signal to eliminate distortion and protect drivers.

Room position compensation: Three pre-set options to optimise sound according to speaker location:

- In a corner

- Against a wall

- Freestanding

Connectivity & user interface

Setup: BeoPlay A9 uses the newest technology available to set up wireless networks using either DLNA or AirPlay technology simply and quickly. Just download the BeoSetup App from the App store, then connect to the wireless network of your choice. No cables are required, as BeoPlay A9 functions as an access point during the setup procedure.

Wireless streaming: Apple AirPlay and DLNA

Line-in: Mini-jack to connect to other audio sources, such as PC, MP3 player or other similar devices

USB: 1 connection

Ethernet: 1 connection

On-device inductive/capacitive touch sensor for volume and mute:

- Swipe a hand across the sensor to turn volume up or down

- Rest a hand on the sensor for a few seconds to mute sound

LED lights: Indicate device and AirPlay status.

iPhone/iPod/iPad: Connect wirelessly, or wired, to iOS devices to control music selection, volume, etc. Will charge an iPhone, iPod or iPad if connected via the USB

Other devices: BeoPlay A9 also includes DLNA technology, which allows wireless streaming from other devices such as Android phones

Setup: Visit www.beoplay.com/support for setup videos and instructions

What’s included

BeoPlay A9 in white with silver front fabric; mains cable; a set of wooden legs; instructions and international warranty.

Photos available for download at http://mediacenter.bang-olufsen.dk/

B&O PLAY from Bang & Olufsen provides premium listening and viewing experiences to digitally connected design fans. For more information, see www.beoplay.com and www.bang-olufsen.com

iPhone, iPod, iPad and AirPlay are trademarks of Apple Inc., registered in the U.S. and other countries.